## Slide 1: BLOB-FREE
PRELIMINARY DESIGN REVIEW (PDR)
Interdisciplinary project A.Y. 2020/21
Proposed by pROf. dovis, prof. piras and prof. di pietra

## Slide 2: BLOB-FREE
Computer vision system for reducing Coronavirus infection risk
MASK detection
ASSEMBLAGE detection

## Slide 3: System CONCEPT
ZED2 Stereo Camera
NVIDIA Jetson Nano
Audio warning
Real-time head detection
Real-time face mask detection
Real-time distances computation
Real-time assemblage detection
Management web interface

## Slide 4: Hardware design
ZED2 Stereo Camera
NVIDIA Jetson Nano
Available resolution/frame rate combinations:
720p – 15, 30, 60 fps
1080p – 15, 30 fps
2K – 15 fps
Computational power:
0.5 TFLOPs (FP16)
128 CUDA cores
(not tested yet)
NVIDIA Quadro P1000
Computational power:
30 TFLOPs (FP16)
640 CUDA cores
Successfully tested up to 2K – 15 fps
Expected maximum resolution usable with the Jetson is 720p – 30fps but testing still needs to be performed

## Slide 5: PERFORMANCE Testing
Lighting conditions
Resolution and frame rate
High illumination with natural lighting
Artificial lighting
Low illumination with natural lighting
Face detection up to 12m
Depth map usable up to 8m
Face detection up to 15m
Depth map usable up to 10m
FOV variation
Brightness variation
Significant image crop at 1080p
Lower frame rates lead to higher brightness

## Slide 6: OBJECT detection & Distance computation

## Slide 7: OBJECT detection & MASK RECOGNITION

## Slide 8: OBJECT DETECTION
ZED person/face detection model:
Built-in the SDK
High computational power requirements
Next steps:
Pre-process images to increase accuracy
Test performance of Jetson Nano

## Slide 9: MASK RECOGNITION
Open dataset (Kaggle):
7555 images (3726 with mask, 3829 without mask)
Transfer learning:
MobileNetV2 model
Trained on Google Colab
Next steps:
Optimize the model
Export the model to work in real-time with ZED SDK

## Slide 10: Management interface
Local web application:
CherryPy
MongoDB
Number of rules violations
Web UI with charts regarding aggregated statistics and system status real-time overview
Percentage of rules violation
Number of people detected

## Slide 11: Workplan
Chart: 
| Project plan definition | User requirements definition | Image recognition methodology evaluation and definition | Training dataset gathering | Cameras testing | Solid image composition algorithm development | Person recognition algorithm | Assamblages detection algorithm | Mask detection algorithm | Statistics visualization | Warning issuing management | Controlled-scenario testing | Results analysis and validation | Real-world scenario testing | Final results analysis
Start Date | 44120 | 44127 | 44141 | 44141 | 44146 | 44169 | 44169 | 44225 | 44225 | 44295 | 44295 | 44323 | 44333 | 44343 | 44350
Duration (days) | 14 | 35 | 21 | 28 | 23 | 56 | 56 | 70 | 70 | 28 | 28 | 10 | 10 | 7 | 22
27/11
SRR
16/10 – 30/10
18/12
PDR
15/1
CDR
7/5
TRR
25/6
FR

## Slide 12: Thank you for the attention!
Team members:
Can Akgol (s274948)
Paolo De Santis (s280398)