## Slide 1: BLOB-FREE
System requirement review (SRR)
Interdisciplinary project A.Y. 2020/21
Proposed by pROf. dovis, prof. piras and prof. di pietra

## Slide 2: BLOB-FREE
Computer vision system for reducing Coronavirus infection risk
MASK detection
ASSEMBLAGE detection

## Slide 3: USER REQUIREMENTS
Facilitate surveillance where the infection risk could be high (e.g. corridors of a university)
Automate warnings for rules violation
Hardware + Software + Web interface

## Slide 4: Technical Requirements
Face detection and localization in 3D space
Convolutional neural network (CNN)
3D distance between heads’ centroids

## Slide 5: Hardware
Raspberry Pi and Pi Camera
  Pros: cheap, small, low power consumption
  Cons: low computational power, lower reliability
ZED2 Stereo Camera and NVIDIA Jetson Nano
  Pros: high computational power, reliability
  Cons: expensive, bulkier, higher power consumption

## Slide 6: Stereolabs ZED2
ZED2 Stereo Camera
  Depth mapping
  Object tracking
  Inertial measurement unit (IMU)
  Neural networks-based SDK exploiting CUDA acceleration (NVIDIA GPU required)
NVIDIA Jetson Nano
  Development board with NVIDIA GPU
DEPTH
B
G
R

## Slide 7: Software
Python
Computer vision:
  Open CV
  Tensorflow
  Numpy
  ZED SDK
Management system:
  CherryPy
  MongoDB

## Slide 8: Camera Testing
Good accuracy (+/- 10 cm) for short distances (1-6 m)
Depth sensing working up to 15 m
Nov. 11, 2020
ZED2 Camera arrived at Politecnico
Nov. 18, 2020
Preliminary test of the SDK
Nov. 25, 2020
Camera test in different conditions and accuracy evaluation

## Slide 9: DEPTH MAP

## Slide 10: Workplan
Chart: 
| Project plan definition | User requirements definition | Image recognition methodology evaluation and definition | Training dataset gathering | Cameras testing | Solid image composition algorithm development | Person recognition algorithm | Assamblages detection algorithm | Mask detection algorithm | Statistics visualization | Warning issuing management | Controlled-scenario testing | Results analysis and validation | Real-world scenario testing | Final results analysis
Start Date | 44120 | 44127 | 44141 | 44141 | 44146 | 44169 | 44169 | 44225 | 44225 | 44295 | 44295 | 44323 | 44333 | 44343 | 44350
Duration (days) | 14 | 35 | 21 | 28 | 23 | 56 | 56 | 70 | 70 | 28 | 28 | 10 | 10 | 7 | 22
27/11
SRR
16/10 – 30/10
18/12
PDR
15/1
CDR
7/5
TRR
25/6
FR

## Slide 11: Thank you for the attention!
Team members:
Can Akgol (s274948)
Paolo De Santis (s280398)